## Slide 1
Summer Learning Series
Webinar 3 of 3 | September 8, 2021
BONNEVILLE POWER ADMINISTRATION
Notes: Photo credit: Julius Jansson on Unsplash

## Slide 2
Org Name
+
Fall Flavor:
Apple or Pumpkin?

## Slide 3: Non-Residential Lighting Sales Data Analysis, 2020

## Slide 4: Non-Residential Lighting Study Activities
Sales Data Collection
Market Intel Gathering
Market Modeling and Momentum Savings
Notes: The nonresidential lighting study is comprised of three core activities: sales data collection and reporting, market intel gathering, and market modeling to estimate momentum savings. The focus of this presentation is the results of the 2020 sales data collection effort that wrapped up earlier this year and how it informs market trends and modeling assumptions.

## Slide 5: Sales Data Collection & Reporting
5
Notes: Sales data collected from distributors is a crucial input to the nonresidential lighting market model. Every year, the team collects data from regional distributors and reports out regional sales trends in an aggregated market results report. At a high level, the purpose of the study is to gather annual sales data from distributors selling nonresidential lighting in the Northwest in an effort to create a dataset that is representative of the total nonres lighting market in the region.

## Slide 6: 8th Year Collecting Distributor Sales Data
Halogen
Linear Fluorescent
HID
Incandescent
LED
CFL
7%
2%
32%
2%
3%
39%
Chart: 
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
LED | 0.06538 | 0.097163 | 0.15304 | 0.27295 | 0.37155 | 0.47843 | 0.52447 | 0.57033
HID | 0.040315 | 0.049226 | 0.04768 | 0.031937 | 0.027595 | 0.021517 | 0.018224 | 0.016995
Linear Fluorescent | 0.63138 | 0.51302 | 0.51265 | 0.46318 | 0.39381 | 0.34194 | 0.31374 | 0.29816
Incandescent | 0.08559 | 0.10317 | 0.079737 | 0.058801 | 0.059727 | 0.044317 | 0.030283 | 0.020684
Halogen | 0.038941 | 0.05123 | 0.037721 | 0.033366 | 0.032901 | 0.020299 | 0.020525 | 0.015177
CFL | 0.1181 | 0.15959 | 0.14649 | 0.11809 | 0.089886 | 0.080735 | 0.076931 | 0.063912
Controls | 0.020287 | 0.026598 | 0.022687 | 0.021674 | 0.024528 | 0.012767 | 0.015828 | 0.01475
Controls
2%
Notes: 2021 was the 8th year collecting distributor sales data from distributors in the Northwest. We’ve collected a lot of data over the years, and the longer we do the study the more valuable it becomes. Sales trends may look flatter from year to year, but looking back to 2013 we can see the impacts of market trends playing out in the data more clearly, which makes it an important regional resource for non-residential lighting market trend reporting and forecasting.
This data is used for regional assessments of the non-res lighting market. Primarily, the goal of the study is to inform the BPA non-residential lighting market model, but the data is also used by other regional entities. For example, the RTF uses the data as an input to their bi-annual non-res lighting mid stream measure, and the final report from this study that details trends in the market is shared in the region as a key resource for understanding market dynamics. In addition, the time series-ed nature of the data set is what makes it so powerful and helps feed the sales mix of products included in the Momentum market model, in addition to other sources like the CBSA.
What's on this slide isn’t all of the data, and we have data going back to 2010, so this has been a valuable resource for the market model and for regional stakeholders.

## Slide 7: Process for Distributor Data Submission
7
Notes: 2021 was the 8th year collecting distributor sales data from distributors in the Northwest. The process to collect sales data requires a few key steps. First, Cadeo works with Evergreen Consulting and NEEA to leverage their distributor relationships and recruit distributors to participate in the study. Then, when distributors agree to participate, Cadeo sends each distributor the data collection materials and guides each distributor through the process of submitting their sales data. After data is submitted, each submission is QC’ed individually to look for errors in data entry or order of magnitude (for example, an accidental entry of 100,000 units instead of 10,000) and then QC’ed against all other collected data to look for inconsistent or unexpected sales trends. When the data has been verified, the distributor is given an incentive to thank them for their time. The final report produced at the end of the study also includes a personalized benchmarking report for each distributor that shows their sales for the year stacked against the average of all collected sales in that year. This report acts as an additional incentive for distributors to participate.

## Slide 8: Disposition of Distributor Outreach
Total distributors included in outreach: 70
Total distributors submitting data: 27
Repeat participants: 22
New participants: 5
Data collected from these 27 distributors represented ~47% of total market unit sales
Notes: Over the course of the study, we have built a database of regional distributors that we treat as the population of all distributors selling nonres lighting products in the Northwest. Each year, we contact as many distributors from that list as possible to request participation in the study, and we ask them to provide data for a set period of time. For example, in 2021 we asked distributors participating for the first time to provide 2016 through 2020 sales data. Previous participants only submit data for years we do not already have (so if they participated last year, we only asked for 2020 data).
In 2021, the team reached out to a total of 70 distributors and 27 ultimately participated, five additional from the 22 participants in 2020. Of the 27 participants, 22 were returning participants and 5 were newly recruited to the study. As a result of this ongoing effort, we have amassed a data set covering data from 2013 through 2020. This includes data from all participants in those study years, both current year participant data and extrapolated previous participant data. In total, 2020 data represents collected and extrapolated data sets from 47 regional distributors.
We estimated that the sales data collected and extrapolated in this year's study represents 47% percent of total market unit count product sales, based on the total market estimates in the non-residential lighting model. The total market we use to make this comparison is the market size indicated in the non-res lighting market model. Cadeo manages this data by collecting distributor data submissions, conducting thorough cleaning and QC, assessing the representativeness of the data, and using our extrapolation methodology to fill in data gaps from inconsistent participation.
Additional note:
We have some data back to 2010, but it isn’t used in analysis

## Slide 9
Distributor Participation Over Time
Chart: 
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Series 1 | 12 | 16 | 27 | 24 | 22 | 22 | 23 | 27
Fewer individual distributors, but more branches represented (i.e., more total data)
Notes: Distributor participation has varied over time. For the most part, distributor participation has been relatively consistent since 2015. The team pursued a strategy to collect regional sales data at the division level from one of the major distributors in the region. So, fewer individual branches participated, but the data collected represented over 40 branches total.
A core goal of the study is to maintain distributor participation year over year. Some distributors do not participate every year due to timing constraints or other extenuating factors, but the team makes an effort to re-engage these distributors in the study where possible. The team also tries to increase participation through recruiting new participants to the study each year. As you can see, we typically get somewhere in the low to mid twenties of distributors participating in a given year.

## Slide 10: Representative Sample of Distributors
Mix of Distributors Submitting Data Compared to the
Pacific Northwest Distributor Population, 2020
Notes: In each year, we strive to ensure our participating distributor sample is a representative mix of distributors from the region. We look at representativeness in two ways. First, this figure shows the mix of participating distributors by relative size, distribution area, and business model compared to the known distributor population mix in the Northwest. This is how we evaluate whether our participating distributor pool is reasonably representative of the total population of distributors in the region. Population data comes from a regional distributor database developed for this study in 2016, which is regularly updated to include participants in the last four years of studies.
This graph shows that for distributors participating in 2021 we saw:
A higher portion of small distributors and a smaller portion of medium and large distributors, relative to the population
A larger portion of local distributors and a smaller portion of national distributors, relative to the population
A slightly smaller portion of Full Line distributors and a slightly larger portion of Lighting Consulting distributors, relative to the population
The representativeness of our sample has changed over time to reflect both changes in the distributor sample and changes in the distributor population. Distribution Area has remained relatively stable year over year, but Relative Size and Business Model have seen more substantial shifts.
Definitions:
Large - more than 10 branches in the Northwest
Medium - between 5 and 10 branches in the Northwest
Small - fewer than 5 branches in the Northwest
Maintenance, repair, and operations (MRO) and online distributors may sell lighting products only or a mix of lighting and other products with a focus on maintenance sales.
Full Line distributors sell a variety of electrical products including lighting.
Lighting consulting distributors focus on energy efficiency products and project-based work. This project-based work includes new construction, renovation, and retrofit sales, and tends to focus on LEDs and lighting control products.

## Slide 11
2017
Chart: 
| Sample | Population
Series 1 | 42 | 25
Series 2 | 4 | 8
Series 3 | 54 | 67
Chart: 
| Sample | Population
Series 1 | 27 | 20
Series 2 | 18 | 10
Series 3 | 55 | 70
2018
Chart: 
| Sample | Population
Series 1 | 18 | 15
Series 2 | 9 | 10
Series 3 | 73 | 75
2019
Chart: 
| Sample | Population
Series 1 | 13 | 15
Series 2 | 9 | 11
Series 3 | 78 | 74
2020
Chart: 
| Sample | Population
Large | 7 | 16
Medium | 4 | 10
Small | 89 | 74
2021
LARGE
SMALL
MEDIUM
Relative Size
Chart: 
| Sample | Population
Series 1 | 23 | 17
Series 2 | 44 | 48
Series 3 | 33 | 35
2018
Chart: 
| Sample | Population
Series 1 | 32 | 32
Series 2 | 41 | 47
Series 3 | 27 | 21
2019
Chart: 
| Sample | Population
Series 1 | 39 | 34
Series 2 | 39 | 46
Series 3 | 22 | 20
2020
Chart: 
| Sample | Population
Large | 48 | 38
Medium | 33 | 43
Small | 19 | 19
2021
LIGHTING CONSULTING
MRO & ONLINE
FULL LINE
Business Model
2017
Chart: 
| Sample | Population
Series 1 | 22 | 16
Series 2 | 46 | 54
Series 3 | 32 | 30
Notes: Looking at Relative Size over the last five years, the distributor population over time has shifted slightly towards smaller distributors and away from larger distributors. Our sample has mirrored this shift but with a more drastic shift away from large participants towards smaller participants.
Similarly, looking at business model, the distributor population has shifted towards lighting consulting distributors slightly over the last five years. Our sample has shifted more drastically towards lighting consultants than the population has. However, the team heard from BPA’s expert panelists for this market, and market intelligence gathered this year, that lighting consultants are becoming more prevalent in the region as LEDs become ever more prolific. These lighting consultants tend to be small distributors, hence the corresponding shift in our sample and the population towards smaller distributors.
While the trends in our participant pool are generally following the trends in the region, it is a goal for next and future years to ensure large, full line participants that may have dropped out over the course of the study are re-engaged to bring our sample into close alignment with the population.

## Slide 12: Data is Representative of the Region
Distributor Lamp Shipments, Floor Space, and Branches by State, 2020
Notes: We also look at whether the data collected from participating distributors is representative of what we expect in the region. This figure shows the lamp sales for 2020 by state, that’s the grey bar, compared to each state’s percentage of total commercial floor space, the blue bar, and known distributor branch locations, the green bar. We use this information to see if our mix of sales by state in the collected data is proportional to what we expect to see in the region. We use floor space and branches as comparisons because we believe these two metrics should approximately correlate with sales. As shown in the figure, collected 2019 lamp sales were roughly proportional to each state’s share of regional commercial floor space and distributor branches.
There is obviously some variation, as the three bars do not align perfectly in each state. But they are approximately proportional, and this confirms that we have reasonable representation from each state. The data has shown strong regional representation over the course of the study.
Additional Note:
The team updated the floorspace distribution by state using the 2019 CBSA report published by NEEA.

## Slide 13
Direct Sales
Distribution
Online/Retail
Lighting sales
Collected sales only represent the distribution sales channel
Notes: It is important to note that collected sales data only represent the distribution sales channel. Market intelligence gathered by the research team indicates that the distribution channel is the largest sales channel for non-residential lighting. However, the sales data collected does not include sales from alternative channels. For example:
  We did not collect sales data from any specialized national account distributors or manufacturers. Despite multiple attempts in this and previous study years to connect with national account distributors, the team has yet to secure participation from any of them. While some participating distributors serve national account customers among other types of customers, previous research on national accounts suggests that many national accounts get their lighting products from specialized distributors that serve national accounts exclusively. It is possible that some lighting consultants serve more national accounts than traditional full-line or MRO & online, but we did not explore this possibility specifically as part of this study. If participation from lighting consulting distributors remains high in future studies, we will explore if having increased lighting consulting representation impacts the representation of national account sales.
  We also did not collect sales data from any specialized online distributors, but some online sales are reflected in the collected data. One long-time online distributor stopped participating in the study in 2018, and since then the team has been unable to collect data from this segment. Last year, we determined through webinars and informal interviews with traditional distributors that most traditional distributors are considering the online sales channel both through their own online sales platforms and through partnerships with third party vendors like Amazon. This year, we added questions to the standard data collection tool to ask what percentage of sales were from online channels and if these sales were from their own websites or through third party vendors. Only 8 of the 27 participants reported online sales, and of those only two sold products through an online third-party vendor. All of the distributors with reported online sales indicated that these sales were included in the sales reported through the standard data collection tool, indicating that the team is already collecting online sales from participating distributors. In future years of the study, we will work to further define the size and importance of this sales channel as well as the percentage of online sales within data already collected in this study.
  We know from conversations with BPA’s expert panelists this year that the distributor landscape is changing. The study team will track these changes and develop strategies for including other sales channel as appropriate in the coming years. We will discuss our goals for future years of the study in more detail in future slides.

## Slide 14: 2020 Sales Trends
Notes: The next several slides highlight some key findings from the 2020 data collected early this year.

## Slide 15: LEDs Continue Gaining Market Share
Percent of Unit Sales by Technology Type, 2016–2020
Notes: Now transitioning to looking at trends in the reported data, this figure shows the percent of all unit sales collected by technology type over the last five years. LEDs have continued to grow year over year, overtaking LFLs (linear fluorescent lamps) for the first time in 2018 and making up more than half of all collected sales in 2019. In 2020, LEDs accounted for 57% of all lighting sales in 2020.
Total volume of unit sales across lighting technologies fell 17 percent between 2019 and 2020 due, at least in part, to the year-over-year increase in market penetration of long-lived LED products. The decrease in unit sales could have been compounded by the effects of COVID-19 on the non-residential lighting market, which slowed construction progress and disrupted supply chains in addition to causing financial hardship for some businesses. Because installed LEDs require less frequent replacement, the team anticipates total unit sales of all lighting technologies to continue to decrease in coming years.

## Slide 16: Sales Mix Varies by Distributor Business Model
Percent Unit Sales by Tech Type Across Business Models, 2016–2020
Full Line
MRO and Online
Lighting Consulting
LED
HID
Linear Fluorescent
Incandescent
Halogen
CFL
Controls
Notes: The technology sales mixes for Full Line and MRO & Online look very similar and have become increasingly similar over time. LEDs have gained market share in these distributor types making up 58 percent of sales in Full Line and 51 percent of sales in MRO & Online in 2020. Lighting consultants looked very different with 85 percent of unit sales coming from LED technologies.
Lighting consulting distributors tend to focus on energy efficiency, and these distributors moved toward LED technologies more quickly. Lighting consulting was the only business model where controls made up a significant portion of sales at 14 percent in 2020, up from 10 percent in 2019.

## Slide 17
Chart: 
| Decorative & Track Lighting | Indoor Fixtures | Outdoor Fixtures | A-Type | Reflectors/Downlights | TLEDs
% of LED Unit Sales | 0.03 | 0.11 | 0.03 | 0.1 | 0.26 | 0.46
TLEDs Make Up 46% of LED Unit Sales
Percent of LED Unit Sales, 2020
Notes: Looking now within the LED product category, TLEDs made up the largest component of LED sales in 2019 at 46 percent. The mix of LED unit sales stayed consistent between 2019 and 2020. However, there was an uptick in market share of TLEDs from 39 percent in 2019 to 46 percent in 2020, while all other LED products saw slight downticks between 2019 and 2020.

## Slide 18: LEDs Steadily Replace CFLs
Downlight Sales by Technology Type, 2016–2020
Notes: The trend of LEDs continually gaining market share is reflected again in the downlight application. For the four downlight products shown, the sales mix continued to shift from CFL pin-based lamps to LED lamp and fixture alternatives in 2020. LED downlight fixtures and retrofit kits continued to steal market share from all lamps. LED technologies made up 60 percent of the downlight application in 2020, an increase from 56 percent in 2019. CFLs represented less than half of downlight sales, declining from 44 percent in 2019 to 40 percent in 2020.

## Slide 19
Percent T8 Replacement Sales by Type, 2016–2020
48% of T8 Replacement Lamps are TLEDs
Notes: Among linear lamps, the sales mix between 4ft T8 linear fluorescent lamps and TLEDs became nearly equivalent in 2020, with 4ft T8 linear fluorescent lamps at 52 percent and TLEDs at 48 percent. Reduced wattage linear fluorescent lamp sales remained high in 2020 at 22 percent of linear lamps. Looking at TLEDs, UL Type B sales (23 percent) continued to exceed UL Type A sales (20 percent) for the second year in a row. UL Type A+B represented 4 percent of the linear lamp category in 2020, and UL Type C represented another 1 percent.

## Slide 20: Ambient Linear Sales are 54% LED
Note:
Sales are normalized to an average of two lamps per fixture
Percent Ambient Linear Lamp and Fixture Sales by Type, 2016–2020
T5 4ft Fixtures
T12 4ft Fixtures
T8 4ft Fixtures
Integrated LED Fixtures
TLED 4ft Fixtures
Notes: In the ambient linear application, LED products continued to replace linear fluorescent products, and LED products made up over half (54 percent) of sales in this application for the first time in 2020. The increase in LED products is driven by an increase in 4ft TLEDs from 34 percent in 2019 to 42 percent in 2020. The market share of integrated LED fixtures decreased for the first time in 2020, after increasing year-over-year 2013-2019.

## Slide 21
Chart: 
| LED | CFL | Halogen | Incandescent
Percent of Screw-In Lamp Sales by Type, 2019 | 0.76 | 0.04 | 0.07 | 0.12
76% of Screw-In Lamp Sales are LED
Percent of Screw-In Lamp Sales by Type, 2020
Notes: Among screw-in products, LED products have consistently grown in market share since 2016 and hold 76 percent market share in 2020. CFLs and halogens continued to lose market share and trend towards insignificance in the sales mix. Incandescents held 12 percent market share in 2020, but changes in regulations could drive incandescent market share down in future years.

## Slide 22: Upcoming Key Dates
Aggregate Report will be published in Q4 2021
Non-residential Lighting Market Model Update will be completed by the end of 2021
2021 data collection will begin in February 2022
Notes: The aggregated sales data report that shows these trends is being finalized this month and will be available in Q4 of this year. Also in Q4 of this year, the modeling team will complete the non-residential lighting market model update and publish results. These results will be folded into the 2022 study by updating our total market estimates. The 2022 study collecting 2021 sales data will begin early next year and we will begin requesting data in February 2022.
https://www.bpa.gov/EE/Utility/Momentum-Savings/Pages/Lighting.aspx

## Slide 23: The Future of Non-Residential Sales Data Collection
Notes: Even though we have conducted this study in relatively the same way year over year, we are constantly seeking to improve our understanding of the market and our approach for collecting representative sales data. The next few slides outline some of our goals for the future of this study.

## Slide 24
  Deepen our understanding of the traditional distribution channel
  Grow our understanding and build strategies for additional sales channels
During the 2021 Plan Period, core goals are:
Notes: 2021 signals a transition out of the 7th plan period and into the 2021 plan period, and the team is working to plan and execute improvements to our processes to ensure we are still collecting high quality and representative data to fold into the 2021 plan period lighting model. Under this new plan period, there are two core goals for the data collection effort:
  First, we will continue to deepen our understanding of the traditional distribution channel through efforts to update firmographic information for the distributor population. This will include understanding distributor population trends through conversations with market experts and researching each participating distributor to understand their business models. The team will make a thorough update to our distributor population database through these two efforts to ensure our population is a true representation of the traditional distributor market in the region.
  Second, we will grow our understanding of all sales channels for nonresidential lighting in the Northwest and build strategies to collect sales from these alternative channels as appropriate. This effort will also involve conversations with market experts to understand how the full landscape of non-residential lighting sales is changing in the region. The team will investigate trends in online sales and non-traditional distributor lighting sales channels to determine if there is an alternative sales channel we should be tracking through sales data collection or other market research strategies.

## Slide 25: Strategies for Recruitment
Maintain participation among traditional distributors
Build participation among national accounts specialists, online sellers, and other specialized sales channels
Notes: Our primary tool to reach these goals is with our outreach and distributor recruitment process. Next year, we will deploy multiple tactics to maintain participation among traditional distributors. We are particularly focused on re-engaging previously participating large, full line distributors to the study to bring our distributor sample into closer alignment with the known distributor population. We will explore strategies like meeting in person (if possible), increased incentives, and longer data submission timelines to bring these distributors back into the study.
We will also explore strategies to build participation among national accounts specialists, online sellers, and other specialized sales channels as appropriate. These distributors may not be incentivized to participate in the same way traditional distributors are. The team will work with market experts to devise a recruitment strategy that addresses these distributors needs and incentivizes participation.

## Slide 26
Chart: 
| Measure Includes Controls | Measure Does Not Include Controls
Sales | 116 | 134
2021 Plan Period Total aMW Savings
Controls are increasing in importance
MEASURE INCLUDES CONTROLS
MEASURE DOES NOT INCLUDE CONTROLS
Notes: Controls represent a large percentage of savings potential in the 2021 plan period. A significant portion of the lighting measures in the 2021 plan include controls (example, converting a linear fluorescent to an LED with controls). While we know controls have been growing in importance in the region, our current controls strategy only minimally collects controls from distributors. Distributors have historically had trouble filling out the controls section of the data collection tool, so the team simplified that section to only ask for photocell, occupancy sensor, and LLLC (luminaire level lighting control) and advanced controls sales. The team will need to devise a strategy to more comprehensively collect controls sales data from distributors or other market actors.

## Slide 27
  Engaging other market actors for insights into controls sales channels and/or sales data
During the 2021 Plan Period, we will explore strategies for collecting controls sales data through:
  Modified/increased efforts with distributors
Notes: Under the 2021 Plan Period, we will explore strategies for collecting controls sales data through:
  Modified/increased efforts with distributors. Considering the 2021 plan combined many lighting measures with controls, the team could modify the LED sales tab to include questions related to how many LED unit sales include or are sold with controls. The team will work with distributors and market experts to understand how distributors track sales of controls in their data and how we may best be able to capture that data in our data collection process.
  There is a chance that distributors are not the right group to collect sales data from. The team will work with market experts to understand the sales channels for controls and how we might engage other market actors for insights into the controls markets and/or to collect controls sales data if possible

## Slide 28
TIM BANKROFF
BPA Project Lead
tjbankroff@bpa.gov
JESSICA AIONA
Subject Matter Expert
jlaiona@bpa.gov
Contact

## Slide 29
Thank you for tuning in to the 2021 Summer Learning Series!
See you on November 3, 2021
www.bpa.gov/EE/Utility/Momentum-Savings/Pages/Calls.aspx
Notes: Photo credit: McKayla Crump on Unsplash