## Slide 1
Section 7 of 10:
Manufactured Homes

## Slide 2: The Basics: Mobile Home Heating System
Duct Location | 
Lengthwise Joists | Main duct installed between floor joists, touching flooring material
Crosswise Joists | Main duct installed below the floor joists
Section 7: Manufactured Homes

## Slide 3: Crosswise Floor Joists
Underbelly drops down in the center
Provides more room in the duct and insulating blanket below the duct
Section 7: Manufactured Homes

## Slide 4: Parts of the Duct System
Most, if not all of this, is within underbelly
Majority accessible from inside home or underneath by disconnecting crossover
Section 7: Manufactured Homes

## Slide 5
Duct BlasterTM Fan Connections

## Slide 6: Duct Blaster Fan Connections
  Four Common Connection Points
  Open Plenum
  Furnace Opening
  Furnace Return
  Supply Register
Section 7: Manufactured Homes

## Slide 7: Open Plenum Connection
Wipe away any dust around base of the plenum (tape will not stick well to dusty surfaces)
Section 7: Manufactured Homes

## Slide 8: Open Plenum Connection
Cover plenum base with a piece of cardboard with a Duct Blaster fan-sized hole; cover all other openings with tape
Section 7: Manufactured Homes

## Slide 9: Open Plenum Connection
Connect Duct Blaster Fan to the cardboard with tape
Section 7: Manufactured Homes

## Slide 10: Furnace Opening Connection
Use piece of cardboard and tape to seal off the return to the furnace
Section 7: Manufactured Homes

## Slide 11: Furnace Opening Connection
Cover opening of the furnace with a piece of cardboard with a hole cut in it where snorkel can attach. Cover all other openings with tape
Section 7: Manufactured Homes

## Slide 12: Furnace Opening Connection
Connect the Duct Blaster snorkel to the cardboard with tape
Section 7: Manufactured Homes

## Slide 13: Furnace Return Connection
Attach the Duct Blaster snorkel to the furnace return; cover any gaps with tape
233
Section 7: Manufactured Homes

## Slide 14: Snorkel to Register Connection
Remove the register cover; set aside
234
Connect Duct Blaster snorkel to the open register using tape. Remember to tape off the return when using this method.
Section 7: Manufactured Homes
Notes: Do not put duct blaster directly on floor like the far right photo

## Slide 15: Repair the Boot
235
Remember to always repair the boot!
Don’t have a mirror? Take a picture with your phone to check boot condition
Section 7: Manufactured Homes

## Slide 16: End Caps
236
Section 7: Manufactured Homes
End caps required on ducts extending beyond last register
Construct using sheet metal or other UL-181 approved rigid material
Seal with mastic

## Slide 17
End Caps:
Step 1: Cut sheet metal scoop a little smaller than needed and place into boot.
Section 7: Manufactured Homes

## Slide 18
End Caps:
Step 2: Screw into place and seal with mastic.
Section 7: Manufactured Homes

## Slide 19
End Caps:
Step 3: Lateral ducts sometimes need end caps too.
Section 7: Manufactured Homes

## Slide 20
End Caps:
Step 4: Screw in place and prep for mastic.
Section 7: Manufactured Homes

## Slide 21
Plenum Seal

## Slide 22: Plenum Connection
Connection below a plenum (view from above)
Close up!
Large Gap
Section 7: Manufactured Homes

## Slide 23
Plenum Connection:
Step 1: Sheet metal straps and screws are used to secure
the cross-over to the duct.
Section 7: Manufactured Homes

## Slide 24
Plenum Connection:
Step 2: Mesh is used to cover the rest of the gap.
Section 7: Manufactured Homes

## Slide 25
Plenum Connection:
Step 3: Finally, all seams around the cross-over to duct are sealed, as well as the furnace to plenum seams.
Section 7: Manufactured Homes

## Slide 26
Use shears to cut a hole large enough to allow access to the interior of the plenum.
Use a duct knife to cut into the plenum. Make this cut directly below the furnace.
Section 7: Manufactured Homes

## Slide 27
Scope for any major leakage. Ensure all the flanges that secure the furnace to the plenum are securely folded over.
247
Section 7: Manufactured Homes

## Slide 28
Apply mastic to the seams were the furnace and plenum connect. Use mesh tape first to cover gaps larger than 1/4 inch.
Section 7: Manufactured Homes

## Slide 29
Apply mastic to the outside seams if there is nothing structural in the way (flooring trusts, 240 volt wiring).
Section 7: Manufactured Homes

## Slide 30
Now repair the opening you made to the plenum by first applying mastic to the edge of the hole you cut.
Section 7: Manufactured Homes

## Slide 31
Using a screw gun, fasten a piece of sheet metal to cover the entire opening. Make sure there are no gaps around the existing hole.
Section 7: Manufactured Homes

## Slide 32
Apply mastic to the edge of the sheet metal cover to ensure a tight seal.
Section 7: Manufactured Homes

## Slide 33
Use screws and washers, or a stapler, to attach a Tyvekä patch over the hole in the belly.
253
Section 7: Manufactured Homes

## Slide 34
Apply mastic to the entire edge of the Tyvek to ensure a tight seal.
Section 7: Manufactured Homes

## Slide 35
Cross-Over Repairs

## Slide 36
Remove the old cross-over duct and any remnants that were used to connect it to the take-off. A clean working surface is needed for a tight seal.
Section 7: Manufactured Homes

## Slide 37
Look for unfolded connection tabs in the interior of the take-off were it connects to the duct.
Section 7: Manufactured Homes

## Slide 38
Fold over any unfolded connection tabs.
Section 7: Manufactured Homes

## Slide 39
Using a screw gun, attach the connection lip to the duct work. Use at least one screw on all four sides to secure it to the duct.
Section 7: Manufactured Homes

## Slide 40
Apply mastic to the duct take-off seam.
Section 7: Manufactured Homes

## Slide 41
Slip the inner lining of the cross-over, around the take-off of the duct work. Slide the lining up far enough so that two loops of the inner lining support are inside the ductwork.
Section 7: Manufactured Homes

## Slide 42
Hand tighten the Panduitä strap around the inner lining of the crossover.
The ribs of the strap should face inside.
262
Use the Panduitä gun to tighten and snip off the excess strap.
Section 7: Manufactured Homes

## Slide 43
Prepare a Panduitä strap for the exterior of the cross-over duct. Place it around the cross-over down from the connection.
Section 7: Manufactured Homes

## Slide 44
Hand tighten the Panduitä strap around the outer lining of the crossover.
Use the Panduitä gun to tighten and snip off the excess strap.
Section 7: Manufactured Homes

## Slide 45
Make sure the cross-over duct is elevated at least 6 inches off the ground.
Section 7: Manufactured Homes

## Slide 46
Carpe Seal ’Em
Section 7: Manufactured Homes

## Slide 47
Section 8 of 10:
Combustion Safety

## Slide 48: Section 8: Combustion Safety
CO Alarm Requirement
Carbon Monoxide
Combustion Safety Plan
Section 8: Combustion Safety

## Slide 49: Combustion Equipment? CO Alarm Required
If there’s anything that burns any fuel in the house or attached structure, the program requires that a CO alarm be installed.
    No matter if it uses gas, propane, fuel oil, wood, etc. – just that it burns something
Section 8: Combustion Safety
Notes:   Even if homeowner has a fireplace that is rarely if ever used and they feel they don’t need a CO detector, it’s still required.

## Slide 50: Combustion Safety Testing Can Include…
Polluting equipment not allowed in a home
Carbon Monoxide (CO) testing
Gas leak testing
Back drafting testing in room with CAZ equipment
Carbon monoxide monitor requirement
Measurement of flue gases
Section 8: Combustion Safety
Notes: Cover the different levels of CAZ testing and what PTCS requires. This exposes them to the different protocols available and they can formulate their own combustion safety plan.

## Slide 51: Affect of Carbon Monoxide (CO)
Section 8: Combustion Safety
Even in small concentrations, it can cause sickness and even death.
PPM CO in air | Symptoms experienced by healthy adults | Comments
Less than 35 ppm | No effect in healthy adults | 35 ppm is WISHA 8-hour average permissible limit
200 ppm | Headache, fatigue, nausea, dizziness | 200 ppm is the WISHA ceiling limit
400 ppm | Severe headache, fatigue, nausea, dizziness, confusion, can be life-threatening after 3 hrs of exposure | 
1,500 ppm | Headache, dizziness, nausea, convulsions, collapse, death within 1 hour | Greater than 1,500 ppm are considered “immediately dangerous to life or health”
3,000 ppm | Death within 30 minutes | 
6,000 ppm | Death within 10–15 minutes | 
12,000 ppm | Nearly instant death | 

## Slide 52: Causes of CO in Homes
Urban Traffic
Cars started in garages
Unvented combustion equipment
Backdrafting combustion equipment
Failed heat exchangers
Section 8: Combustion Safety
General Rule
If there is combustion, there might be CO
Corroded and cracked furnace heat exchanger

## Slide 53: Unvented Combustion Equipment: Not Safe
Section 8: Combustion Safety

## Slide 54
Large amounts of heat energy are released during the combustion process
Section 8: Combustion Safety
CO By-Product of Incomplete Combustion

## Slide 55
A lower rate of dilution
Back drafting of combustion equipment
Build up of CO in the home
Section 8: Combustion Safety
Potential Negative Effects of Duct Sealing
Duct Sealing companies should have a plan to reduce liability

## Slide 56
When air is heated the molecules move further apart making it less dense than the surrounding air.
Denser air pushes the lighter air up the vent.
Why Category I Appliances Vent
Section 8: Combustion Safety

## Slide 57
The driving force that moves a hot air balloon up is the same driving force that vents the gas water heater.
Buoyancy, not heat.
Section 8: Combustion Safety
Buoyancy Creates Draft Pressure

## Slide 58: Driving Forces That Make Air Move
Wind
Stack (Chimney Effect)
Exhaust Fans
Duct Leakage
Unbalanced Forced Air Systems (interior door closure)
Section 8: Combustion Safety

## Slide 59: Competing Pressures
Driving forces compete for the same air
Draft is a very weak force; loses out to stronger pressures
Section 8: Combustion Safety

## Slide 60
Turning on exhaust fans and leaky supply ducts outside the house can create negative pressure in the room where the combustion equipment is located.
  May cause combustion gases to be pulled down the flue
Section 8: Combustion Safety
DO NOT Create Back Drafting Problems
  Back drafting combustion appliances can produce large amounts of CO, often in the thousands of parts per million.

## Slide 61
Section 9 of 10:
Participation Rules & Paperwork

## Slide 62
Section 9: Participation Rules & Paperwork
Next Steps to Certification
Online Account
Technician Application
Entering a Job into the Mobile Registry
Quality Assurance Inspections

## Slide 63: Next Steps to Certification
Section 9: Participation Rules & Paperwork
Step 1
Pass this training’s exam
Step 2
Create online account on ptcs.bpa.gov
Step 3
Submit Certified Technician Application found in “How to Participate” section on www.bpa.gov/goto/reshvac

## Slide 64: Step 2: Create Online Account Now!
Section 9: Participation Rules & Paperwork
Go to ptcs.bpa.gov and click “Register” to create a profile.
Mobile view
Desktop view
Account will be activated and tech ID assigned when all the steps are completed.

## Slide 65: Step 3: Certified Technician Application
Section 9: Participation Rules & Paperwork
Find it at the end of your Trainee Manual or in “How to Participate” section on www.bpa.gov/goto/reshvac
Submit photos or scans of completed & signed application by email to ResHVAC@bpa.gov or fax it to 1-877-848-4074
Note: Submit this form when tech is new, receives additional training, or needs to update company info.

## Slide 66: Next Steps: Some Clarification
A non-PTCS Certified technician can seal the ducts, but a PTCS certified technician must perform the leakage tests and inspect the duct sealing.
Certification will follow you to any company. Submit new Certified Technician Application to update information.
Section 9: Participation Rules & Paperwork

## Slide 67: Beyond Certification
Enter in Online Registry*
Test and Seal Ducts
Submit Documentation to Utility
May qualify for a Quality Assurance Inspection
Get Certified
Section 9: Participation Rules & Paperwork
*Enter using mobile device with internet access or use the optional form for later entry

## Slide 68: Entering a Job: Online Registry
Section 9: Participation Rules & Paperwork
Log in to installing technician’s account at ptcs.bpa.gov and click “Enter a Project” or click “Contractors” and select “Enter a Job”.
For a guide on entering a job online, see page 19 in your Trainee Manual.
Mobile view

## Slide 69: Mobile Registry Updates
Online registry optimized for use on any mobile device
  Not an app you download
Save progress function to complete entered data later
  Enter job data before, during, and after installation by saving your progress
Times out after 4 hours of inactivity
Informational bubbles explaining some program components
Some limitations
  No offline entry mode. Can’t use without internet access.
  Optional forms available to record data for later entry, but not required to submit.
Section 9: Participation Rules & Paperwork

## Slide 70: Exercise: Optional Mobile Entry Practice
Go to test site on a mobile device: https://ptcs.test.bpa.gov
  Only a test environment. Nothing will publish live on this site.
Sign in:
  Username:TestContractor
  Password: Ptcs1234
Enter a job:
  Active physical address
  Enter any data. Some suggestions:
    Pre-test Ring 1, Fan Pressure 86 Pa, and CFM 382
    Post-test Ring 3, Fan Pressure 140 Pa, and CFM 74
Section 9: Participation Rules & Paperwork

## Slide 71: Registry Entry Tip!
Upon entry into the registry, enter the correct duct blaster fan pressure and not the house test pressure of 50 Pa.
If you do this, your house may be rejected
The registry calculates the flow in CFM using:
  Ring Size
  Fan Pressure
Fan Pressure ≠ House Pressure
Section 9: Participation Rules & Paperwork

## Slide 72: Troubleshooting Entry Issues
Section 9: Participation Rules & Paperwork
Contact the PTCS team if:
  Address isn’t validating
  Need to enter in a second system
  Can’t find an entered job
  Need to edit an address or submitted data
  Need immediate review of “Pending” entry (reviewed regularly)

## Slide 73
Section 9: Participation Rules & Paperwork
If no internet or mobile device is available or the job cannot be entered online for any reason, this form is available to record the data for later entry.
Can be found on ptcs.bpa.gov and at the end of your manual.
Optional PTCS Duct Sealing Form
* Some participating utilities require installation form, please check with utility prior to job submission

## Slide 74
Technician or company required to notify the utility of the completed job.
Contact customer’s utility for information on required paperwork.
Utilities have access to the online registry and are able to review completed job details.
Notifying Utility of the Completed Job
Section 9: Participation Rules & Paperwork

## Slide 75: Quality Assurance Inspections
At least 10% of all jobs are inspected for:
  Measured Leakage
  CO Detector Installed, if required
  Crossover (Manufactured Home)
  Sealing and Repairing Air Handler to Plenum
  Ducts in Good Repair
  Joints Fastened
  Tape Removed and/or Covered with Mastic
  Ducts Sealed
  Duct Insulation Re-installed
Section 9: Participation Rules & Paperwork
Notes:   We try to QA the first 3 jobs a contractor submits. Some utilities do this some do not.

## Slide 76: QA Inspection Feedback & Remediation
Section 9: Participation Rules & Paperwork
Inspection feedback will be communicated to the technician and/or their company. See the “PTCS Technician Support Plan” at the end of your Trainee Manual for what to expect if a project does not pass inspection.

## Slide 77
Section 10 of 10:
Resources

## Slide 78: Program Website
All of the following are on this website: https://ptcs.bpa.gov
  Specifications
  Requirements
  Technical and Training Resources
  Online Registry Resources
  Link to Online Marketing Portal
  Installation Forms
Section 10: Resources
Notes: Tech and training resources include: Equipment setup diagrams and equipment conversion tables

## Slide 79: Program Website: Technical Resources
Go to the “PTCS and Prescriptive Duct Sealing” section on www.bpa.gov/goto/reshvac
Technical Resources for Duct Sealing include:
  Leakage Testing Diagrams
  Blower Door Set Up Diagram
  Flow Conversion Tables
Section 10: Resources

## Slide 80
Spanish Materials
Now available in Spanish:
  PTCS training presentations
  Manuals
  Tests
  Forms
Contact Eli Caudill at CLEAResult: eli.caudill@clearesult.com
Section 10: Resources
300

## Slide 81: Equipment Discount
Discount now available to purchase duct testing equipment:
  12.5% discount for Blower Door and Duct Blasters from TEC
  12.5% discount for digital gauges from TEC
Discount form included at the end of your Trainee Manual
Submit this form to Eli Caudill at CLEAResult: eli.caudill@clearesult.com
Section 10: Resources

## Slide 82: Stay Informed!
Sign up for the Quarterly Newsletter or visit the PTCS website for the latest announcements
  Updated specifications
  Online registry changes
  Common issues in the field
  Updated program requirements
  New technical support resources
  Tips and tricks
We guarantee we will not spam you or sell any of your information.
Go to https://tinyurl.com/ptcsnewsletter
or email ResHVAC@bpa.gov to sign up. Also sign up from the “Stay Informed!” link on the website.
Section 10: Resources

## Slide 83
New Training Tools and Support
New LMS site: https://clearesult.moodle.school/login/index.php
      Admin/Sales Webinar
      Heat Pump Sizing Webinar
Section 10: Resources

## Slide 84
Good luck on the Exam!
Questions?
Comments?
Contact the PTCS Team:
Phone: (800) 941-3867
Email: ResHVAC@bpa.gov

## Slide 85: Energy Trust of Oregon Jobs
For questions concerning PTCS installations for customers of Pacific Power or Portland General Electric, please call 1-866-365-3526 or email Residentialforms@energytrust.org.