## Slide 1: Resource Program Enhancement Project
Needs Assessment and Optimization Model Workshop
November 9, 2017

## Slide 2: Introductions and Agenda

## Slide 3: Background
BPA began doing its Resource Program after the Act was passed in 1980
The purpose of RP is to assess BPA’s need for power and reserves and then develop a resource strategy for meeting those needs
BPA did the RP until 1992 after which it relied on its 1995 business plan
In 2008, after BPA signed 20 year contracts, it restarted the RP process
Over the past couple of years, BPA has been reviewing its methods for planning and has identified some areas of change which will be discussed today
The proposed changes should enhance many of its long-term planning activities through augmented information and analysis

## Slide 4: Project Scope
An update to the Resource Program includes the following efforts
  Change to end use based load forecasting
  Conducting a BPA conservation potential assessment and distributed energy resources potential assessment
  Reviewing the Needs Assessment
  Determining the economic evaluation methodology and tool for resource optimization
Decisions about resource acquisitions are beyond the scope of the Resource Program as it is not a decision-making process or document. The Resource Program provides information BPA can use to make informed resource acquisition decisions in the future.

## Slide 5: Project Goals
Long Term Goal
  Develop a sustainable and repeatable process that enhances the analysis of the BPA Resource Program including informing other processes such as
    Integrated Planning
    Transmission Planning
    Power Planning
    Non-wires Planning

## Slide 6: Resource Program Planning Process
Needs Assessment Metrics*
* Indicates a new process

## Slide 7: Needs Assessment

## Slide 8: Resource Program Planning Process
Needs Assessment Metrics*
* Indicates a new process

## Slide 9: Needs Assessment Overview
The Needs Assessment provides forecasts of Federal system energy, capacity, and balancing reserve needs
  Considers federal system resources and load obligations
These results inform later steps of the Resource Program process
The Needs Assessment methodology is largely unchanged from previous Resource Programs, however, the study is being expanded to a 20 year continuous forecast and will use the frozen efficiency load forecast

## Slide 10: Needs Assessment Major Assumptions
Post-2028 Power Sales Contracts
  Continuation of Tiered Rates Methodology and Regional Dialogue Contracts
  Plus and minus need sensitivities
Columbia River Treaty
  2020-2024 Assured Operating Plan and associated Canadian Entitlement
Spill Operations
  2014 Biological Opinion
FCRPS Balancing Reserve Requirement
  BP-18 Final Proposal amounts of 602 MW Inc/729 MW Dec
Hydro Project Generator Outages
  Updated forecast for 2020-2039

## Slide 11: Needs Assessment Metrics
Annual Energy
P10 Heavy Load Hour
P10 Superpeak
18-hour Capacity
Balancing Reserves

## Slide 12: Needs Assessment Metrics
Annual Energy
  Evaluates the annual energy surplus/deficit under 1937-critical water conditions
  Studies will provide a 20 year continuous forecast

## Slide 13: Needs Assessment Metrics
P10 Heavy Load Hour
  Evaluates the 10th percentile (P10) surplus/deficit over heavy load hours by month, given variability in hydro generation, loads, and Columbia Generating Station performance
  Each month is analyzed independently
  Studies will provide a 20 year continuous forecast

## Slide 14: Needs Assessment Metrics
P10 Superpeak
  Evaluates the 10th percentile (P10) surplus/deficit over the six peak load hours per weekday by month, given variability in hydro generation, loads, and Columbia Generating Station performance
  Each month is analyzed independently
  Studies will provide a 20 year continuous forecast

## Slide 15: Needs Assessment Metrics
18-Hour Capacity
  Evaluates the ability to meet the six peak load hours per day over a three-day extreme weather event assuming median water conditions
  Winter and summer extreme weather events are analyzed
  Both seasons assume maximum take of the Canadian Entitlement, zero wind generation, and limited market reliance
  Winter events assume reduced streamflows due to the effects of icing
  Summer events assume reduced Columbia Generating Station output due to adverse weather conditions
  Studies will provide forecasts for 5 years that span the 20 year horizon

## Slide 16: Needs Assessment Metrics
Balancing Reserves
  In the past the Needs Assessment has evaluated the ability to meet forecasted balancing reserve demand in Bonneville’s balancing authority area
  Due to significant uncertainty, the upcoming Needs Assessment will likely provide a qualitative analysis of balancing reserve demand

## Slide 17: Wellness Break

## Slide 18: Optimization Model

## Slide 19: Resource Program Planning Process
Needs Assessment Metrics*
* Indicates a new process

## Slide 20: Optimization Model Overview
All resource options are evaluated against our market price forecast on an hourly basis for each risk iteration (Performance Run)
Optimization attempts to meet all specified needs across all iterations at the lowest cost (Portfolio 1)
Numerous other portfolios will be generated with different portfolio cost and risk levels
Market Price Forecast
Needs Assessment
Market Limits
All Available
Options
Performance Run
Optimization
Portfolio 2
Portfolio 3
Portfolio 4
Portfolio 5
Portfolio 6
Portfolio 7
Portfolio 8
Portfolio 9
Portfolio 10
Portfolio … n
Portfolio 1
AURORA Process

## Slide 21: Price Forecast
AURORA is a production cost model used by BPA in every rate case since 2000
We model all of the Western Interconnection at the zonal level
Start with a resource build generated by:
  Existing and high likelihood additions / retirements compiled from multiple sources
  Add renewable buildout sufficient to meet RPS targets
    CA 50% by 2030, incremental needs met by 80% in state solar
    OR 50% by 2040 (varies by utility—effectively closer to 35%)
Add CA behind the meter solar consistent with CA Energy Commission (CEC) forecast
Use AURORA long term capacity expansion logic to make economic retirements and ensure there are sufficient thermal resources to meet planning reserve margins throughout Western Interconnection over forecast duration

## Slide 22: Price Forecast
For each study we typically produce 3,200 forecasts of monthly diurnal prices based on a single resource build
  3,200 = 40 forecasts for each of 80 water years
Model variation around:
  Loads
  Hydro generation
  Natural gas prices
  Wind generation
  Transmission availability
  CGS generation
Portfolio optimization will likely have 800-1600 iterations (higher run resolution means more computation time and much greater storage requirements)
Market Price Forecast
Distribution
Forecast
Historical
INPUT DB
AURORA!
x3200
WECC Loads
FERC 714
50 Hourly
250 Monthly
500 Yearly
Henry Hub
Platts Gas Daily
875 Monthly
NG Bases
HYDSIM&
HOSS - PNW
80 Water Years
COI, PDCI, BC TX
CA Wind
PNW Wind
WECC
Existing
Renewables
CGS White Book
3200 Monthly
30 Hourly
Legend
Sim
100 Hourly
BC Hydro
33 Water Years
AURORA Thermal Resource Build
30 Hourly
CA Hydro
39 Water Years

## Slide 23: Inputs—Supply Options
Supply-side generating resources
  Costs and technical characteristics representative of reference plants used in the development of the 7th Power Plan.
    CCCTs, SCCTs, Frames, Recips, Wind, Utility-scale solar
  Non-dispatchable resources rely upon exogenous output shapes.
    - Solar shapes based upon NREL data
    - Wind shapes based upon BPA’s wind-risk models

## Slide 24: Inputs—Supply Options
Demand-side resources:
  Conservation
    BPA specific CPA of measure savings and cost will develop EE supply curves
    No pre-screening: All technically achievable measures considered, although we will aggregate into bundles for modeling efficiency.
  Other DERs:
    Demand response, batteries, etc. Currently contracted with Cadmus in support of developing DER supply curves.

## Slide 25: Performance Run
All possible supply options are evaluated on an hourly basis for each input price iteration
  Dispatch and commitment decisions are made based on input market price forecast
    EE units are set to must run
    Storage resources and DR will perform on price (may need to adjust performance depending on behavior we get)
  Options to include emission rates & prices within the performance run for dynamic calculation of avoided carbon emission benefits (as opposed to assuming a fixed rate and netting off the cost of the unit)
Total output, costs, and benefits are aggregated into monthly diurnal buckets for the optimization

## Slide 26: Optimization
Given exogenous needs data (both energy and capacity), the model will select among the total resource stack a combination of resources that meet the energy need, such that the whole portfolio cost is minimized, while observing the planning reserve margin constraints.
We can (and will) allow the model to choose a variety of portfolios that meet needs, but allow departures from a single cost minimization portfolio to construct a risk / reward tradeoff curve.
The result, will be a set of portfolios that define an efficiency frontier.

## Slide 27: Efficiency Frontier
Chart: Risk (Std Dev of Total Portfolio Cost)
| 101 | 101.61051 | 102.48832 | 103.71293 | 105.37824000000001 | 107.59375 | 110.48576 | 114.19856999999999 | 118.89568 | 124.76098999999999 | 132 | 140.84101000000001 | 151.53632000000002 | 164.36342999999999 | 179.62624 | 197.65625 | 218.81376000000003 | 243.48907000000005 | 272.10367999999994 | 305.11149
 | 1000000 | 997500 | 995000 | 992500 | 990000 | 987500 | 985000 | 982500 | 980000 | 977500 | 975000 | 972500 | 970000 | 967500 | 965000 | 962500 | 960000 | 957500 | 955000 | 952500

## Slide 28: Results of Optimization Process
Portfolios solved by the optimization process are used to inform resource acquisition strategies as determined by the Administrator
Results of the optimization process are not binding constraints on future BPA resource decisions.
Consideration of the efficiency frontier facilitates a discussion of the qualitative differences between different portfolio strategies, while incorporating a robust risk-informed methodology.

## Slide 29: Key Issues
1 | Approach to Scenario Analysis
2 | Price Forecast
3 | Balancing reserves supplied by FCRPS (discussed earlier)
4 | Juvenile bypass spill operations assumptions (discussed earlier)
5 | Hydro Assumptions (discussed earlier)
6 | Years included for 18 hour capacity study (discussed earlier)
7 | Post-2028 power sales contract assumptions (discussed earlier)
8 | Percentage of EE that reduces the BPA load obligation
9 | Transmission & Distribution Deferral Value
10 | Risk Mitigation Credit
11 | Cost of Carbon
12 | EE Costs and Benefits
13 | Candidate list of resources for supply curves
14 | Bundles for EE Supply Curves
15 | CPA Technical and Achievable Potential
16 | Market reliance assumptions

## Slide 30: Estimated Project Timeline

## Slide 31: Discussion Q&A